## Slide 1: T04: Self Leveling Table
Sean Hendrickson
Waleed Alhaddad
Adrian Steele
Taylor Griffin

## Slide 2
Self Leveling Table: Level 0
Self Leveling Table
Power,
6 VDC
Table Top
Leveled
LED angle display
Gravitational Accelerative Force
Module | Self Leveling Table
Inputs | Gravitational Accelerative Force: The external forces acting on the device, used to determine the angle of the device and set servo position Power: 6 VDC from batteries.
Outputs | Table Top Leveled: the top tray will become leveled using servos. LED angle display: Decorative LED display based on each servo’s position. Using SPI interface. System Status: 4 LEDs representing transmission and error statuses. Using 3.3 V GPIO from microcontroller.
Functionality | - Consists of 2 layers, the base, housing the batteries, PCB, servos, and LEDs, and the top tray which will be leveled by servos. Receives input from an accelerometer and determines servo position to keep the top tray level.
System Status

## Slide 3
Microcontroller
Servo Controller
Voltage Regulator
6V to 3.3V
LED Strip
Servo 1
Voltage Regulator
6V to 5V
Self Leveling Table Design: Level 1
Servo 2
Servo 3
Gravitational Accelerative Force
Power,
6 VDC
Leveled table
LED angle display
Accelerometer
Status LEDs
System Status
Oscillator
Logic level shifter
TWI
LED strip
control
Servo
positions
Shifted servo positions
Shifted LED
Strip control
PWM signal
5 VDC
3.3 VDC
Status info
clock

## Slide 4
Accelerometer: Level 0
Accelerometer
Power,
3.3 VDC
TWI
Module | Accelerometer
Inputs | Gravitational Accelerative Force: The accelerative force acting on the accelerometer Power: Regulated 3.3 VDC Initialization: Set 50 Hz sample rate, fast read mode (ignore last 4 data bits for x y z output), and activate output. Communicated via TWI
Outputs | x y z values: 8 most significant bits of 12, expressed in 2’s complement, representing 1 of 256 values on a ± 2 g scale transmitted over TWI
Functionality | - Measures the accelerative forces, and outputs the values of the x y z directions.
Gravitational Accelerative Force

## Slide 5
Voltage Regulator 6V to 3.3V: Level 0
Voltage Regulator
6V to 3.3V
Module | Voltage Regulator 6V to 3.3V
Inputs | 6 V battery power supply
Outputs | Regulated 3.3 VDC
Functionality | - Lowers the incoming 5-20 volts down to a regulated 3.3 VDC, outputting up to 500 mA
Power,
6 VDC
Power,
3.3 VDC

## Slide 6
Voltage Regulator 6V to 5V: Level 0
Voltage Regulator
6V to 5V
Module | Voltage Regulator 6V to 5V
Inputs | 6 V battery power supply
Outputs | Regulated 5 VDC
Functionality | - Lowers the incoming 6-26 volts down to a regulated 5 VDC, outputting up to 1 A
Power,
6 VDC
Power,
5 VDC

## Slide 7
Microcontroller: Level 0
Microcontroller
Module | Microcontroller
Inputs | Power: Regulated 3.3 VDC Clock: 8 MHz TWI x y z input: 8 most significant bits of 12, expressed in 2’s complement, representing 1 of 256 values on a ± 2 g scale transmitted over TWI
Outputs | LED Strip Control: Decorative LED display based on each servo’s position. Communicated via SPI Status info: 4 LEDs representing transmission and error statuses. Using 3.3 V GPIO Servo position: send servo number and corresponding pulse width value. Communicated via USART
Functionality | - Converts x y z values to angles. Runs calculation of correct servo position based on input provided by accelerometer. Also sends LED strips configurations based on current servo positions. Displays system status via 4 LEDs on PCB
Power,
3.3 VDC
Status info
TWI
Clock
Servo Positions
LED Strip Control

## Slide 8
Logic level shifter: Level 0
Logic level shifter
Module | Logic Level Shifter
Inputs | Power: Regulated 5 VDC LED Strip Control: LED display signals coming from microcontroller Servo position: servo position signals coming from microcontroller
Outputs | Shifted LED Strip Control: Shifted LED signals from 3.3 to 5 V Shifted Servo position: Shifted servo position signals from 3.3 to 5 V
Functionality | - Shifts signals coming in from the microcontroller to a 5 V output
Power,
5 VDC
Shifted servo positions
Servo
positions
LED strip
control
Shifted LED strip control

## Slide 9
Oscillator: Level 0
Oscillator
Module | Oscillator
Inputs | 
Outputs | Clock: 8 MHz
Functionality | - Sends the microcontroller an 8 MHz clock pulse
Clock

## Slide 10
Status LEDs: Level 0
Status LEDs
Module | Status LEDs
Inputs | - Status Info: High or low signal depending on which LEDs to turn on. Communicated via 3.3 V GPIO
Outputs | - System status: 4 LEDs that light up on PCB
Functionality | - Displays status information including what transmissions are occurring (TWI, USART) and any errors
System status
Status Info

## Slide 11
Servo Controller: Level 0
Servo Controller
Module | Servo Controller
Inputs | Power: Regulated 5 VDC Servo positions: pulse width values in quarter µs (integer) and target servo. Communicated via USART
Outputs | Servo positions: Pulse width modulation signal to corresponding servo
Functionality | - Creating pulse width modulated signals to control up to 12 servos.
PWM signal
Power, 5 VDC
Servo positions

## Slide 12
LED Strip: Level 0
LED Strip
Module | LED Strip
Inputs | Power: Regulated 5 VDC LED Strip control: which LEDs to light up. Communicated via SPI
Outputs | LED Angle Display: 15 LEDs lit up in different configurations
Functionality | - Decorative LED display based on each servo’s position. Should not consume more than 1 A. Multicolored.
LED Angle Display
Power, 5 VDC
LED Strip control

## Slide 13
Servos: Level 0
Servos
Module | LED Strip
Inputs | Power: 6 VDC PWM signal: pulse width modulation signal to specify what point to position the arm
Outputs | Leveled table: Adjust servo positions to level the top tray
Functionality | - The servo position is determined by the main program so that they keep the tray balanced. Range of 45°
Leveled Table
Power, 6 VDC
PWM signal

## Slide 14: UML: Activity Diagram
Power on device
Set servos to home position
Initialize accelerometer
Sample Accelerometer
Convert accelerometer data to angles
Calculate servo positions
Send positions to servos
Update LED strip
Servo movement delay
Repeat until powered off
*Note: Update status LEDs after every communication and calculation and in the event of an error.

## Slide 15: UML: Interaction Diagram
Microprocessor
Accelerometer
Status LEDs
LED Strip
Servo Controller
Servos
2. Update Status
1. Set servos to home position
4. Initialize Accelerometer
3. Move servos
5. Update Status
6. Request accelerometer data
7. Transmit accelerometer data
8. Update Status
10. Send positions to servos
9. Calculate
servo positions
12. Move servos
11. Update Status
13. Update LED Strip
14. Update Status
15. Repeat steps 6 - 15