## Slide 1: Team 04 – Self Leveling Table
Sean
Waleed
Adrian
Taylor

## Slide 2: Problem or Need
Suitable project for practicum.
Waiters sometimes drop their tray’s contents.
Hard to keep things balanced.

## Slide 3: Motivation
Get a good grade!
Resume material.
Good practice for capstone and career.
Cool gadget to play with.
Useful to keep things balanced.

## Slide 4: Objective
Keep a tray level in real time.
Create working prototype in 10 weeks.
Entertaining to play with.

## Slide 5: Alternatives

## Slide 6: Marketing Requirements
The device should be easily held with two hands.
The device should hold an object on the table to balance.
The device should be responsive.
Should be simple and intuitive to use.
Should be visually appealing.
Should be inexpensive.
Should be safe.

## Slide 7: Constraints
Must have at least one input (sensor) and at least one output (actuator).
Must have at least 2 layers on PCB.
Must have a microprocessor located on PCB.
Must have more than 25% surface mount components (1206).
Must have top-side silk screen.
Must not start from existing design file.
Must have live documentation and use revision control.
Must be published with MIT license.

## Slide 8: Engineering Requirements
Functionality
  The device should maintain a level position while powered on.
Performance
  The device should level itself within 5 degrees.
  Should move to a level position within 2 seconds of becoming unleveled.
  Table should remain level up to 15 degrees relative to the horizontal.
Economic
  Total parts cost will not exceed $200.

## Slide 9: Engineering Requirements
Energy
  The system will should run off batteries for at least 1 hour.
Health & Safety
  Power system and components should be inaccessible to user.
Environmental
  Should be manufactured with lead free solder.
Manufacturability
  PCB should be greater than 1.5 sq. inch and smaller than 140 sq. inches.

## Slide 10: Engineering Requirements
Operational
  Device should be smaller than a cubic foot.
  Device should not weigh more than 5 lbs.
Reliability & Availability
  Table should hold .25 lb. without breaking.
Social & Cultural
  Should have visual feedback system to relay angle state to user.
Usability
  User should not need instructions to use device.

## Slide 11: Our Approach
Triangular base with triangular top tray.
Three servos attached on the corners of the tray.
Receive input from an accelerometer and process in a microprocessor.
Send updated positions to servos based on device tilt.
Battery powered for portability.
Lots of LEDs for entertainment.

## Slide 12: Initial Concept

## Slide 13: Servo Brackets

## Slide 14: PCB & Battery Placement

## Slide 15: Base to Servo Brackets Mounting

## Slide 16: Tray to Base Assembly

## Slide 17: Base Assembly
Base attached with aluminum standoffs
Acrylic side panels used for LED mounting

## Slide 18: Final Design

## Slide 19
Self Leveling Table: Level 0
Self Leveling Table
Power,
6 VDC
LED angle display
Gravitational Accelerative Force
Module | Self Leveling Table
Inputs | - Gravitational Accelerative Force: The external forces acting on the device, used to determine the angle of the device and set servo position - Power: 6 VDC from batteries.
Outputs | - LED Angle Display: 15 LEDs lit up in different configurations. Lights up based on device tilt slowly changing colors. LEDs around the device become more blue on the device side that is tilted up. LEDs around the device become more red on the device side that is tilted down. - System status: 4 LEDs that light up on PCB. First LED is green, displays when tilt on the x axis reaches its limit. Second LED is yellow, displays when there is communication between the microcontroller and the servo controller. Third LED is yellow, displays when there is communication between the microcontroller and the accelerometer. Fourth LED is red, displays when the tilt on the y axis reaches its limit.
Functionality | - Consists of 2 layers: the base (two triangular acrylic sheets enclosing the batteries, PCB, servos, and LEDs), and the top tray (one triangular acrylic sheet leveled by servos). Receives input from an accelerometer and determines servo position to keep the top tray level.
System Status

## Slide 20
Microcontroller
Servo Controller
Voltage Regulator
6V to 3.3V
LED Strip
Servo 1
Voltage Regulator
6V to 5V
Self Leveling Table Design: Level 1
Servo 2
Servo 3
Gravitational Accelerative Force
Power,
6 VDC
LED angle display
Accelerometer
Status LEDs
System Status
Oscillator
Logic level shifter
Accelerometer Initialization
LED strip
control
Servo settings and
positions
Shifted servo positions
Shifted LED
Strip control
PWM signal
specifying servo arm
position
5 VDC
3.3 VDC
Status info
clock
x y z
values

## Slide 21: UML: Activity Diagram
Power on device
Initialize and set servos to home position
Initialize accelerometer
Sample Accelerometer
Convert accelerometer data to angles
Calculate servo positions
Send positions to servos
Update LED strip
Delay
Repeat until powered off
*Note: Update status LEDs after every communication and calculation and in the event of an error.
If servo positions different by 4 degrees or more
Yes
No

## Slide 24: Code
1400 Lines of C
More than 50% reused from manuals or examples online.
Most time consuming.

## Slide 25: Code – TWI Communication
TWI  consists of two signal lines SDA and SCL
Manual sheet is the main resource
TWI to enable two way connection between microcontroller and accelerometer
  Initialize TWI(I2C) in Atmega328 and setup a serial clock to 400kHz
  Generate TWI start signal
  Send a byte through TWI
  Read a byte from TWI, send an acknowledgment back
  Check status register of the TWI

## Slide 26: Code – Accelerometer
Format of TWI communication (read and write) provided by MMA8452Q Accelerometer user manual
  Write (initialization): start condition, 0x3A (slave address of device, mode), 0x2A (register to write to – system control register 1), 0x07 (800 Hz sample rate, reduce noise, fast read mode, active), stop condition
  Read: Start condition, 0x3A (slave address of device), 0x01 (register to start reading from – OUT_X_MSB), repeated start condition, 0x3B (slave address of device, mode), acknowledge each byte, no acknowledge to stop reading

## Slide 27: Code – USART
Used to communicate to Servo controller
Transmission and initialization functions come from example C code from ATmega328 manual and specifications from Pololu Servo Controller user manual
  Initialization: set baud rate (9600), set format of messages (8 bit, 1 stop bit, no parity, asynchronous mode), enable transmitter
  Transmission: make sure transmit buffer is empty, put byte into transmit buffer

## Slide 28: Code – Servo Controller
What needs to be transmit provided by Pololu Servo Controller user manual (SetTarget, SetSpeed, SetAcceleration,SetMultipleTargets)
  Pololu Protocol: 0xAA (baud rate indication byte), 0x0C (device number), command byte (with most significant bit cleared), command data
  SetTarget: 0x84 (command), channel number, target low bits, target high bits
  SetSpeed: 0x87 (command), channel number, speed low bits, speed high bits
  SetAcceleration: 0x89 (command), channel number, acceleration low bits, acceleration high bits
  SetMultipleTargets: 0x9F (command), num targets, first channel num, first target low bits, first target high bits, second target low bits, …

## Slide 29: Servo Position Calculation
Consists of 2 parts:
  Servo angle to tray height
  Distance the tray is off from the home position

## Slide 30: Adafruit Dotstar
Dotstar vs. NeoPixel
Easy interfacing
Adjustable length
Arduino Library

## Slide 31: SPI Communication
1 Byte per pixel
15 pixels total

## Slide 32: Main Program Flow
Initialize the LED strip
  Set initial colors
  output to LED strip
Initialize the Servo Controller
  Initialize USART in microcontroller
  Set speed of servos
  Set all servos to home position
Fill Lookup table with servo angle to height mappings
Initialize the accelerometer
  Initialize microcontroller for TWI communication
  Change settings in Accelerometer

## Slide 33: Main Program Flow
Sample accelerometer
  Sample 400 times and take average
  Blink the accelerometer communication yellow status LED
Update the green and red status LEDs
Servo adjustment
  Calculate distance off from home position
  Search through table to find correct servo angle position
  Update LED strip based on servo angle positions
  Move servos if they are 4 degrees or more off from previous position
  Servo movement delay
Repeat from sample accelerometer

## Slide 34: Tools Used
SolidWorks
Eagle
Atmel Studio
  AVR Dragon Programmer
GitHub
  Repository
  Wiki
LID
  Laser Cutting Acrylic
  Soldering Stations and Oven

## Slide 35: IP and Prior Work
Atmel Code (atmega328 datasheet)
  TWI Interfacing
  USART Interfacing
Internet Search Code
  BlinkLED (Testing initial setup)
    electroSome (https://electrosome.com/blinking-led-atmega32-avr-microcontroller/)
  Binary Search Algorithm
    Programming Simplified (http://www.programmingsimplified.com/c/source-code/c-program-binary-search)
  LED Strip Control
    Adafruit (https://learn.adafruit.com/adafruit-dotstar-leds/overview)
  Accelerometer Data Conversion
    Sparkfun (https://github.com/sparkfun/MMA8452_Accelerometer/blob/QC-Rev/Firmware/MMA8452Q_BasicExample/MMA8452Q_BasicExample)
Arduino
  Angle – PWM Mapping
    Arduino Servo Library

## Slide 36: IP and Prior Work
Lots of YouTube videos with examples.
  https://www.youtube.com/watch?v=ZrZodwEHjew
  https://www.youtube.com/watch?v=T0SFAdPUUYs
  https://www.youtube.com/watch?v=5uR34U1qc-Q
  https://www.youtube.com/watch?v=K-F_T59ZDPw
  https://www.youtube.com/watch?v=uERF6D37E_o
  https://www.youtube.com/watch?v=enlQMUE9df4
  https://www.youtube.com/watch?v=j4OmVLc_oDw

## Slide 37: Testing
Functional Test
  Materials needed:
    Arduino
    Arduino IDE
    Arduino accelerometer example code
  Verify accelerometer outputs valid measurements
  Verify servos are operable
  Verify Servo controller operates servos
  Verify LED strip operation
  Verify microcontroller operation
  Run full system leveling test

## Slide 38: Testing
Integration Test
  Materials needed:
    Atmel Studio
    AVR Dragon Programmer
  Microcontroller to Servo controller (USART) communication
  Accelerometer to Microcontroller (TWI) communication
  Microcontroller level shifting (buffer)

## Slide 39: Testing
Parametric Test
  Materials needed:
    Oscilloscope
    Multi-meter
  Output voltage from voltage regulators
  External oscillator frequency
  Range of servos

## Slide 40: Testing
Stress Test
  Materials needed:
    Randomly distributed weights
  Test maximum tray weight

## Slide 41: Results
Most things worked well.
Servo arms could work better.
LEDs are nice and bright.
Rx on Microprocessor from servo controller Tx not stepped down to 3.3V.
No resets.
Need better errors and cleaner code.

## Slide 42: Contributions
Sean
  Mechanical Design, LED Strip control code, GitHub guru.
Waleed
  TWI Code, Servo arm assembly.
Adrian
  Servo arm design, torque calculations, USART code, servo position algorithm, code formatting.
Taylor
  Hardware design, schematic, layout, soldering, LED strip angle color code.
Everyone!
  Homework, testing, assembly, coding something.

## Slide 43: Lessons Learned
What did we learn?