## Slide 1: T04: Self Leveling Table
Sean Hendrickson
Waleed Alhaddad
Adrian Steele
Taylor Griffin

## Slide 2
Self Leveling Table: Level 0
Self Leveling Table
Power,
6 VDC
LED angle display
Gravitational Accelerative Force
Module | Self Leveling Table
Inputs | - Gravitational Accelerative Force: The external forces acting on the device, used to determine the angle of the device and set servo position - Power: 6 VDC from batteries.
Outputs | - LED Angle Display: 15 LEDs lit up in different configurations. Lights up based on device tilt slowly changing colors. LEDs around the device become more blue on the device side that is tilted up. LEDs around the device become more red on the device side that is tilted down. - System status: 4 LEDs that light up on PCB. First LED is green, displays when tilt on the x axis reaches its limit. Second LED is yellow, displays when there is communication between the microcontroller and the servo controller. Third LED is yellow, displays when there is communication between the microcontroller and the accelerometer. Fourth LED is red, displays when the tilt on the y axis reaches its limit.
Functionality | - Consists of 2 layers: the base (two triangular acrylic sheets enclosing the batteries, PCB, servos, and LEDs), and the top tray (one triangular acrylic sheet leveled by servos). Receives input from an accelerometer and determines servo position to keep the top tray level.
System Status

## Slide 3
Microcontroller
Servo Controller
Voltage Regulator
6V to 3.3V
LED Strip
Servo 1
Voltage Regulator
6V to 5V
Self Leveling Table Design: Level 1
Servo 2
Servo 3
Gravitational Accelerative Force
Power,
6 VDC
Leveled table
LED angle display
Accelerometer
Status LEDs
System Status
Oscillator
Logic level shifter
Accelerometer
Initialization
LED strip
control
Servo
settings
and
positions
Shifted servo positions
Shifted LED
Strip control
PWM signal
specifying
servo arm
position
5 VDC
3.3 VDC
Status info
clock
x y z
values

## Slide 4
Accelerometer: Level 0
Accelerometer
Power,
3.3 VDC
x y z values
Module | Accelerometer
Inputs | - Gravitational Accelerative Force: The accelerative force acting on the accelerometer - Power: Regulated 3.3 VDC - Accelerometer Initialization: Set 50 Hz sample rate, fast read mode (ignore last 4 data bits for x y z output), and activate output. Communicated via TWI. TWI format - send start condition, send accelerometer slave address (0x3A), send register to write to (0x23 - system control register 1), send value to put in register (0x23 - bit 5 = 1 bit 4 = 0 bit 3 = 0 data rate to 50 Hz, bit 1 = 1 fast read mode, bit 0 = 1 active mode), send stop condition.
Outputs | - x y z values: 8 most significant bits of 12, expressed in 2’s complement, representing 1 of 256 values on a ± 2 g scale transmitted over TWI
Functionality | - Measures the accelerative forces, and outputs the values of the x y z directions.
Gravitational Accelerative Force
Accelerometer Initialization

## Slide 5
Voltage Regulator 6V to 3.3V: Level 0
Voltage Regulator
6V to 3.3V
Module | Voltage Regulator 6V to 3.3V
Inputs | 6 V battery power supply
Outputs | Regulated 3.3 VDC
Functionality | - Lowers the incoming 5-20 volts down to a regulated 3.3 VDC, outputting up to 500 mA
Power,
6 VDC
Power,
3.3 VDC

## Slide 6
Voltage Regulator 6V to 5V: Level 0
Voltage Regulator
6V to 5V
Module | Voltage Regulator 6V to 5V
Inputs | 6 V battery power supply
Outputs | Regulated 5 VDC
Functionality | - Lowers the incoming 6-26 volts down to a regulated 5 VDC, outputting up to 1 A
Power,
6 VDC
Power,
5 VDC

## Slide 7
Microcontroller: Level 0
Microcontroller
Module | Microcontroller
Inputs | - Power: Regulated 3.3 VDC - Clock: 8 MHz - x y z input: 8 most significant bits of 12, expressed in 2’s complement, representing 1 of 256 values on a ± 2 g scale transmitted over TWI
Outputs | - LED Strip control: which LEDs to light up. Communicated via SPI. Send 24 bit color pattern, shifted through the strip. - Status info: 4 LEDs representing transmission maximum tilt statuses. Using 3.3 V GPIO. 1 green LED displaying when the tilt on the x axis has reached its limit. 2 yellow LEDs displaying when there is communication between the microcontroller and the accelerometer/servo controller. 1 Red LED displaying when the tilt on the y axis has reached its limit. - Servo settings: Set the speed of the servos. speed limit is given in units of (0.25 μs)/(10 ms). Communicated via USART. Incoming communications can have varying baud rates but the ideal baud rate is 9600. Transmissions must follow the pololu protocol format and be transmitted one byte at a time (0xAA baud rate detection byte, 0x0C device ID of servo controller, 0x07 command byte to set servo speed, <channel number> channel of the servo that you want to set the speed, <servo speed MSB> least significant byte of speed value, <servo speed MSB> most significant byte of speed value) - Servo positions: pulse width values in quarter µs (integer) and target servo to move. Communicated via USART. Incoming communications can have varying baud rates but the ideal baud rate is 9600. Transmissions must follow the pololu protocol format and be transmitted one byte at a time (0xAA baud rate detection byte, 0x0C device ID of servo controller, 0x04 command byte to set servo positions, <channel number> channel of the servo that you want to set the position of, <servo position LSB> least significant byte of PWM value, <servo position MSB> most significant byte of PWM value) - Accelerometer Initialization: Set 50 Hz sample rate, fast read mode (ignore last 4 data bits for x y z output), and activate output. Communicated via TWI. TWI format - send start condition, send accelerometer slave address (0x3A), send register to write to (0x23 - system control register 1), send value to put in register (0x23 - bit 5 = 1 bit 4 = 0 bit 3 = 0 data rate to 50 Hz, bit 1 = 1 fast read mode, bit 0 = 1 active mode), send stop condition.
Functionality | - Converts x y z values to angles. Runs calculation of correct servo position based on input provided by accelerometer. Also sends LED strips configurations based on current servo positions. Displays system status via 4 LEDs on PCB
Power,
3.3 VDC
Status info
x y z values
Clock
Servo Positions
LED Strip Control
Accelerometer Initialization
Servo settings

## Slide 8
Logic level shifter: Level 0
Logic level shifter
Module | Logic Level Shifter
Inputs | Power: Regulated 5 VDC LED Strip Control: LED display signals coming from microcontroller Servo position: servo position signals coming from microcontroller
Outputs | Shifted LED Strip Control: Shifted LED signals from 3.3 to 5 V Shifted Servo position: Shifted servo position signals from 3.3 to 5 V
Functionality | - Shifts signals coming in from the microcontroller to a 5 V output
Power,
5 VDC
Shifted servo positions
Servo
positions
LED strip
control
Shifted LED strip control

## Slide 9
Oscillator: Level 0
Oscillator
Module | Oscillator
Inputs | 
Outputs | Clock: 16 MHz
Functionality | - Sends the microcontroller an 8 MHz clock pulse
Clock

## Slide 10
Status LEDs: Level 0
Status LEDs
Module | Status LEDs
Inputs | - Status Info: High or low signal depending on which LEDs to turn on. Communicated via 3.3 V GPIO
Outputs | - System status: 4 LEDs that light up on PCB. First LED is green, displays when tilt on the x axis reaches its limit. Second LED is yellow, displays when there is communication between the microcontroller and the servo controller. Third LED is yellow, displays when there is communication between the microcontroller and the accelerometer. Fourth LED is red, displays when the tilt on the y axis reaches its limit.
Functionality | - Displays status information including what transmissions are occurring (TWI, USART) and any errors
System status
Status Info

## Slide 11
Servo Controller: Level 0
Servo Controller
Module | Servo Controller
Inputs | - Servo settings: Set the speed of the servos. speed limit is given in units of (0.25 μs)/(10 ms). Communicated via USART. Incoming communications can have varying baud rates but the ideal baud rate is 9600. Transmissions must follow the pololu protocol format and be transmitted one byte at a time (0xAA baud rate detection byte, 0x0C device ID of servo controller, 0x07 command byte to set servo speed, <channel number> channel of the servo that you want to set the speed, <servo speed MSB> least significant byte of speed value, <servo speed MSB> most significant byte of speed value) - Power: Regulated 5 VDC - Servo positions: pulse width values in quarter µs (integer) and target servo to move. Communicated via USART. Incoming communications can have varying baud rates but the ideal baud rate is 9600. Transmissions must follow the pololu protocol format and be transmitted one byte at a time (0xAA baud rate detection byte, 0x0C device ID of servo controller, 0x04 command byte to set servo positions, <channel number> channel of the servo that you want to set the position of, <servo position LSB> least significant byte of PWM value, <servo position MSB> most significant byte of PWM value)
Outputs | - Servo positions: Pulse width modulation signal to corresponding servo. Generates a pulse of a certain frequency to send to the servo what position it should hold. Done automatically, just need to receive input on what position to set the servo to.
Functionality | - Creating pulse width modulated signals to control up to 6 servos.
PWM signal
Power, 5 VDC
Servo positions

## Slide 12
LED Strip: Level 0
LED Strip
Module | LED Strip
Inputs | Power: Regulated 5 VDC LED Strip control: which LEDs to light up. Communicated via SPI. Send 24 bit color pattern, shifted through the strip.
Outputs | Power: Regulated 5 VDC LED Strip control: which LEDs to light up. Communicated via SPI. Send 24 bit color pattern, shifted through the strip.
Functionality | - Decorative LED display based on each servo’s position. Should not consume more than 1 A. Multicolored.
LED Angle Display
Power, 5 VDC
LED Strip control

## Slide 13
Servos: Level 0
Servos
Module | LED Strip
Inputs | - Power: 6 VDC - Servo positions: Pulse width modulation signal to corresponding servo. Generates a pulse of a certain frequency to send to the servo what position it should hold. Done automatically, just need to receive input on what position to set the servo to.
Outputs | Leveled table: Adjust servo positions to level the top tray
Functionality | - The servo position is determined by the main program so that they keep the tray balanced. Range of 140°
Leveled Table
Power, 6 VDC
PWM signal

## Slide 14: UML: Activity Diagram
Power on device
Set servos to home position
Initialize accelerometer
Sample Accelerometer
Convert accelerometer data to angles
Calculate servo positions
Send positions to servos
Update LED strip
Delay
Repeat until powered off
*Note: Update status LEDs after every communication and calculation and in the event of an error.
If servo positions different by 4 degrees or more
Yes
No

## Slide 15: UML: Interaction Diagram
Microprocessor
Accelerometer
Status LEDs
LED Strip
Servo Controller
Servos
1. Set servo speed and move them to home position
4. Initialize Accelerometer
3. Move servos
6. Request accelerometer data
7. Transmit accelerometer data
8. Update Status
10. Send positions to servos if previous
Position differs by 4 or more degrees
9. Calculate
servo positions
12. Move servos
11. Update Status
13. Update LED Strip
15. Repeat steps 6 - 15